| ENGINE START: EXPERIMENTAL: N813GP |
| --- |
| PRE-FLIGHT CHECKLIST | COMPLETE |
| HARNESS(ES) & PFD’S | FASTENED (VERIFY PASS) |
| FUEL SHUT-OFF VALVE | VERIFY ON |
| AVIONICS | OFF (3 SWITCHES) |
| MASTER SWITCH | ON |
| ELECTRIC FUEL PUMP | ON (FOR STARTING) |
| STROBES | ON |
| PROPELLER | “CLEAR’ |
| THROTTLE | CRACK ½” |
| CHOKE | AS NEEDED IF COLD |
| IGNITION SWITCH | START |
| OIL PRESSURE | CHECK 12- 100 PSI |
| ELECTRIC FUEL PUMP | OFF |
| GPS/COM, TRANSPONDER, INTERCOM, TURN COORD | ON AND SET COM CHECK AS NEEDED |
| TAXI LIGHT | ON |
| BRAKES | TEST ON TAXI |
| PRE-TAKEOFF RUNWAY OR WATER |
| FLAPS | SECOND POSITION-20 Deg. |
| TRIM | FULL NOSE UP (2 POB) |
| ELECTRIC FUEL PUMP | ON |
| BILGE PUMP | AS REQUIRED |
| OIL PRESSURE & TEMP | >29 PSI & >120F |
| FUEL GAGE | VERIFY OKAY |
| MAG CHECK @ 3500 RPM: | < 300 RPM DROP/SMOOTH |
| ELECTRICAL GAGE CHECK | 13.6V, & CHARGING |
| GEAR ALERT SYSTEM | PRESS TO TEST, VERIFY |
| CIRCUIT BREAKERS | CHECK |
| FLIGHT CONTROLS | FREE AND CORRECT |
| BRS MORTAR PIN | REMOVE TO PANEL |
| CANOPIES | CRACKED (CLOSE-WATER) |

| TAKE OFF & CLIMB: N813GP |
| --- |
| FULL THROTTLE | RIGHT RUDDER FOR P Factor ROTATE AT 50 MPH CLIMB AT 70 MPH |
| GEAR-RAISE | UnLOCK, LOOK, LIGHT= BLUE |
| FLAPS: | 10 THEN 0 AT CRUISE ALT. |
| FUEL PUMP: | OFF ABOVE 500’ |
| TAXI LIGHT | OFF EXCEPT FOR TRAFFIC |
| PRE-LANDING: RUNWAY OR WATER |
| FLY NORMAL PATTERN | ANNOUNCE: RUNWAY OR WATER LANDING |
| BRIEF PASSENGER | HARNESS, EQUIP STOWED, STERILE COCKPIT RULE |
| CANOPY | RUNWAY: AS REQ’D WATER: CLSED UNLATCHED |
| FUEL PUMP: | ON |
| TAXI LIGHT | ON |
| “GIFT” | Downwind, Base, Short Final |
| GEAR CHECK: Downwind, Base, & Final | LOCK- LOOK- LIGHT SAY ALOUD “Gear UP for Water” |
| IAS: | 70 MPH |
| FLAPS | 20 |
| TRIM | DOWN TO COMFORTABLE |
| SHORT FINAL | 70-80 MPH |
| CHECK GEAR LIGHTS | RED--RUNWAY BLUE--WATER |
| POST-LANDING: |
| FUEL PUMP | OFF |
| FLAPS | UP |
| TAXI LIGHT OFF | STROBES: ON |
| TRIM: | FULL UP |
| AVIONICS-4 ITEMS | OFF |
| MASTER SWITCH | OFF |
| IGNITION SWITCH | OFF, STOW KEY |
| BRS SAFETY PIN | STOW |
| HOBBS METER | RECORD |

| PRE-FLIGHT WALK AROUND CHECKLIST (V1.0) N813GP |
| --- |
| A. ENGINE OIL CHECK: |
| PROPELLER | PULL THROUGH 4 TURNS |
| PROPELLER | NICKS, CRACKS, SECURE |
| CARBURETORS | SECURE |
| PIPES AND HOSES | SECURE |
| EXHAUST, MUFFLER, SPRINGS | SECURE |
| COOLANT LEVEL, COLOR | CORRECT |
| ENGINE MOUNTS | SECURE |
| ELECTRICAL CABLES | CHECK |
| WHEELS | CHOCK |
| AVIONICS | OFF (3 SWITCHES) |
| MASTER | ON |
| ELECTRIC FUEL PUMP | ON |
| STROBES | ON |
| PROPELLER | “CLEAR” |
| CHOKE | AS NEEDED |
| THROTTLE | ½” |
| IGNITION SWITCH | START ENGINE, CHK OIL P. |
| RUN ENGINE | 3 MINUTES |
| FUEL PUMP, MASTER | OFF |
| IGNITION, STROBES | OFF |
| OIL LEVEL | CHECK-CAUTION: HOT! |
| B. COCKPIT & FORWARD FUSELAGE: |
| FLIGHT MANUAL & DOCS | ABOARD |
| IGNITION SWITCH | OFF |
| HOBBS METER | RECORD TIME |
| MASTER | ON |
| FUEL QUANTITY CHECK | BOTH GAGE AND VISUAL |
| ELECTRIC TRIM | CHECK AND SET |
| BILGE PUMP | CHECK, DRAIN HULL |
| MASTER SWITCH | OFF |
| GEAR SAFETY LOCK | LOCKED, SECURE |
| FLIGHT CONTROLS | FULL & FREE MOTION |
| AILERONS PUSH RODS, BOLT ENDS AND CABLES | SECURE |
| FUEL TANK SUMP (IF EQUIP) | DRAIN AND INSPECT |
| STATIC PORTS (2) | CLEAR |
| HULL AND UNDERSIDE | FREE OF DAMAGE |
| C. STARBOARD WING: |
| TIRE INFLATION, CONDITION | SECURE |
| LWR STRUT/FUSELAGE ATTACHMENT BOLTS | SECURE |
| OUTER & JURY STRUT | SECURE |
| WING FLOAT, BRACES | SECURE |
| AILERON OUTER PUSH-PULL ROD | ATTACHED, SECURE |
| AILERON MOVEMENT | FREE |
| FLAP & PUSH-PULL | SECURE |
| WING TO FUSELAGE CABLE | SECURE |
| GASCOLATOR | DRAIN AND INSPECT |
| D. EMPENNAGE: |
| STAB LE TRIM ATTACHMNT | CHECK BOTH SIDES OF FIN |
| ELEV PUSH-PULL TUBE/HORN | CHECK SECURE |
| UPPER & LOWER TAIL CABLES | SECURE |
| TAIL WHEEL INC INFLATION | SECURE & CORRECT |
| E. PORT WING: |
| ALL 8 S/B WING ITEMS ABOVE | CHECKED AS ABOVE |
| FUEL CAP | SECURE |
| PITOT COVER & TUBE | REMOVED & CLEAR |
| TAXI LIGHT | SECURE |