SECTION 4 . NORMAL PROCEDURES

DAILY PRE-FLIGHT INSPECTION

Cockpit & Forward Fuselage

Flight Manual & Maintenance Release			IN A/C

Control Lock 					REMOVE

Ignition Switch					OFF

.	Master Switch					0N

Fuel Quantity & Gauge				VIEW

Electric Trim 					OPERATE

Bilge Pump 					OPERATE

Drain Bung					IN

Master Switch					OFF

Carburettor Heat 					FREE

Undercarriage Over centre				LOCKED

Flight Controls					FULL & FREE

Aileron Push Rods, Both Ends & Cables		SECURE

Fuel Filter/Glass Bowl, Leaks & Contamination		CLEAR

Instruments 					CHECK

Static Ports					CLEAR

Windscreen					CRACKS / CLEAN

Fuel Tank Water/Contamination 			DRAIN

Ensure Stb wing is lowest and a minimum of 350 mls is drained

Drain Tap					OFF

Seat Bells & Inertia Reels - Secure & Functional		CHECK

Hull Sides & Underside - Free of Damage.		CHECK

Coolant Radiator & Opening 				CLEAR

Wing Fabric Surfaces.				CHECK

Necessary Equipment for Water Operations

Licence, Flotation equip, Ropes, Paddles	 	IN A/C

Starboard Wing

Tyre 						CHECK

Lower Strut/Fuselage Bolts				SECURE

Outer Strut & Jury Strut Attachment			SECURE

Pitot Tube clear of Obstruction-Cover 			REMOVED

Wing Float, Braces & 				SECURE

Aileron Outer Push/Pull Rod Attachment		SECURE

Aileron Movement					FREE

Flap & Push/Pull Attachment				SECURE

Wing to Aft Fuselage Brace Cable			SECURE

Wing Tie-Downs					REMOVE

Engine

Oil Level (Run engine for 3 mins prior to checking)	LEVEL

Propeller - Nicks, Cracks & Security			CHECK

Carburettor Attachment & Induction System		SECURE

All Pipes & Hoses - Leakage, Wear & Security		CHECK

Exhaust& Muffler Springs, Cracks& Attachment		CHECK

Coolant Level & Colour				CHECK

Engine Mounts					SECURE

Electrical Cables - Wear & Security			CHECK

Empennage

Stabilizer Leading Edge Trim Attachment		CHECK

Elevator Push/Pull Tubes & Horn Attachment		CHECK

Elevators & Rudder - Free Movement & Security 	CHECK

Upper & Lower Cables				SECURE

Tail wheel for inflation & wear			CHECK

Tail Tie-Down					REMOVE

Port Wing

same Checks as for the Starboard Wing:		CHECK

Fuel Cap Securely Attached				CHECK

COCKPIT SECURITY

Before starting the engine and conducting any operation, ensure THAT

all articles and equipment are stowed safely and secured.

BEFORE STARTING ENGINE

Pre-flight Inspection				COMPLETE

Pull Through Prop - Minimum 6 Revolutions		COMPLETE

Seat Belts & Shoulder Harness Adjusted		CHECK

Fuel Selector Valve					0N

All Radio Equipment & Avionics Power		OFF

Brakes or Chocks as Required			SET

Circuit Breakers In					CHECK

NOTE- Leave VHF & DG, OUT as not in use

STARTING ENGINE

Master Switch					0N

Set Choke for cold start (none for warm start)		FULL ON

Electric Fuel Pump					0N

Throttle - Cold Start

Closed. (If Open, Choke ineffective)			CLOSED

Warm Start

Open (5mm)					OPEN

Propeller Area					CLEAR

Ignition Switch 					START

Oil Pressure					RISING

When engine running smoothly / Choke		OFF

Throttle to idle RPM				1800

Radio & Electrical Equipment			0N

BEFORE TAKEOFF 	(LAND OPS)

Hatches (closed but not locked during water operation)	SET

Seat Belts & Shoulder Harness on			SECURE

Trim - Dual-Full Up, Solo-75% Up for Take-off		SET

Fuel Valve					0N

Fuel - Quantity Double Check			LITRES

Fuel Pump					0N

Flaps 						20’

Engine Run Up 					4,000 RPM

L & R Ignition (RPM drop - not to exceed 300)	CHECK

* Carburettor Heat - note RPM Drop		GREEN

* Engine Instruments (Temps) & Ammeter	GREEN

* Minimum Oil Temperature 			50’ C

Throttle IDLE					1,400 RPM

Radios, Frequencies etc.				SET

Transponder					S/BYE

Strobe Lights					ON

Clearance					AS REQD

BEFORE TAKEOFF -	 (WATER OPS)

Undercarriage UP & LOCKED			UP

Bilge Pump					ON/OFF

Passenger Briefing - 3 H's & Life Jacket		COMPLETE

Waterway Take-Off Path				CLEAR

TAKEOFF

Throttle Maximum 					5800 RPM

Elevator forward to lift tail (Back for Water Ops)		AS REQD

Correct Nose Up Attitude (Water Operation)		CHECK

Lift Off                                       			40 - 45 knots

Accelerate to                                       			50 knots

Climb out, when Established 		Undercarriage.	UP

At Safe Height 				Flaps	10’.

At 500’					Flaps	0’

ENROUTE CLIMB

Airspeed						55 KIAS

Throttle						5500~RPM

Flaps 						UP

Fuel Pump					OFF

CRUISE

Throttle			4900 - 5200 RPM		As reqd

Speed						70-80 kts

Trim						AS REQD

DESCENT

Fuel Contents					CHECK

Throttle Set					AS REQD

Carburettor Heat 					ON

DOWN WIND

Canopies Closed But Not Locked			CHECK

Seat Belts & Shoulder Harness			SECURE

Instruments, Temps, Pressures, Indications		CHECK

Carburettor Heat					ON

Fuel Contents					CHECK

Fuel Pump					ON

Undercarriage For 		Ground Landing		DOWN

Over Centre Lock			CHECK

Undercarriage For 		Water Alighting		UP

Over Centre Lock			CHECK

Flaps 			Turning Base		10’

Waterway, Touch Down Point & Landing Run		CLEAR

BASE LEG

Airspeed Approach					55 - 60 knots

Flaps 						10'

Undercarriage	-IDENTIFY POSITION		CHECK

FINAL APPROACH

Airspeed						50 - 55 knots

Flaps						20’

Undercarriage - 	IDENTIFY POSITION		CHECK

Carburettor Heat					OFF

Canopies Closed But Not Locked			CHECK

Touch Down Point & Landing Run			CLEAR

LANDING - (WATER OPERATIONS)

Undercarriage - 	IDENTIFY POSITION - 		UP

Touch Down Point & Landing Run			CLEAR

Touchdown - CARE in Glassy water conditions		40-45 kts

When carrying out a Touch & Go Landing (especially during water operations)

make sure to set trim Full Up before applying Take-Off Power.

AFTER LANDING

Flaps						UP

Fuel Pump					OFF

Strobe Lights					OFF

AFTER LANDING –

Water Operations - Docking & Beaching

In the case of Docking or Beaching the following points are recommended

to assist in effective & safe operation.  Note: The following procedures should

be carded out only when the aircraft has settled in the displacement mode

and is being operated in idle water taxy.

Radio						OFF

Headsets						REMOVE

Seat Belts & Harness				RELEASE

Undercarriage	 DOWN/UP & LOCKED		AS REQD

Canopies						OPEN

Ropes						READY

Ignition - When Required				OFF

Master Switch					OFF

SHUT DOWN

Radio						OFF

All Electrical Equipment				OFF

Ignition Switch					OFF

Master Switch					OFF

Fuel Valve					OFF

SECURING AIRCRAFT

All Radio & Electrical Equipment			OFF

Ignition Switch					OFF

Master Switches					OFF

Fuel						OFF

Controls 						LOCKED

Canopies						LOCKED

Pitot Tube Cover					ON

Chocks						LOCATED

Tie-Downs					ON

Cockpit/Engine Covers				Fitted